## Slide 1
Smart Trolley Intelligence Platform
ESP32-S3 Edge
AWS RDS MySQL
MQTT TLS 1.3
Open-Meteo
Metabase Analytics
ELEC0033 · UCL Year 3 · Edge Demonstration

## Slide 2
SYSTEM ARCHITECTURE
Three-Tier Edge Deployment
01
INFRASTRUCTURE
2× MKR1010 + 1× ESP32 C3
· 2× MKR1010 + 1× ESP32 C3 Super Mini as static Wi-Fi APs
· SSIDs: ANCHOR_A · ANCHOR_B · ANCHOR_C
· Fixed positions in store
· Trolley passively scans RSSI every 15 s
· Forms indoor positioning grid
02
EDGE LAYER
ESP32-S3 on Trolley
· 50 Hz sensor loop (20 ms)
· 8 on-device classifiers — no cloud inference
· Haptic actuator + TFT display alerts
· MQTT TLS 1.3 publish at 10 Hz
· Continues locally if cloud offline
03
CLOUD / DASHBOARD
AWS + FastAPI + React
· MQTT broker: mqtt.yungcz.com:8883
· AWS RDS MySQL (eu-west-2)
· FastAPI + WebSocket: api.cartly.yungcz.com
· Metabase: analytics.cartly.yungcz.com
· Open-Meteo weather enrichment
→
→

## Slide 3
REQUIREMENTS
User Requirements & Performance Indicators
User / Role
Requirement
Store staff
Real-time alerts when trolley enters checkout queue
Store staff
Immediate notification on pickup or drop
Store manager
Historical analytics: zone utilisation, events, movement
Operator
Adjust detection sensitivity remotely — no physical access needed
Operator
Live health status of every deployed trolley at a glance
System
Battery-powered and untethered — fits trolley form factor
System
Data persisted centrally for cross-session analysis
System
Edge processing continues if cloud connectivity is lost
Telemetry Rate
10 Hz
100 ms MQTT
Event Latency
40 ms
Priority upload
IMU Sample Rate
50 Hz
20 ms loop
Battery Runtime
3.5 hr
1100 mAh @ 1W
MQTT Reconnect
<1.5 s
Firmware retry
DB Columns
28
All labelled

## Slide 4
HARDWARE · SENSING
Four Sensor Types
QMI8658 · 3-axis · 50 Hz
01
IMU Accelerometer
· Linear accel X/Y/Z (mg)
· Dynamic accel — gravity removed
· Pickup threshold: 2.5 m/s²
· Drop threshold: 4.0 m/s²
· Step cadence from peak detection
· Vibration RMS via EMA
QMI8658 · 3-axis · 50 Hz
02
IMU Gyroscope
· Angular velocity X/Y/Z (dps)
· Turn rate EMA for queue detection
· Carry style orientation tracking
· Yaw for dead-reckoning position
· Same chip — distinct modality
Wi-Fi 2.4 GHz · every 15 s
03
RSSI Scanner
· RSSI from ANCHOR_A/B/C (dBm)
· Log-distance path loss model
· Zone: A / B / C / BETWEEN
· 2D trilateration (posX, posY)
· Gaussian KDE heatmap
Magnetic · GPIO ISR · 50 Hz
04
Wheel Encoder
· 3 counts per revolution
· Wheel ⌀ 45.2 mm (caliper-verified)
· Resolution ≈ 47 mm per count
· Signed speed (direction-aware)
· EMA-smoothed · ISR protected

## Slide 5
EDGE INTELLIGENCE
On-Device Behaviour Classification
All 8 classifiers run locally on the ESP32-S3 — no cloud round-trip required for actuation
Carry Style
Algorithm: 5-state rule-based
Inputs: Speed · pitch/roll · vibration · aDyn
LIFTED / PARKED / TILTED_PUSH / ROUGH_ROLL / SMOOTH_ROLL
Pickup Detection
Algorithm: aDyn threshold > 2.5 m/s²
Inputs: Accelerometer
→ 200 ms haptic + cloud event flag
Drop Detection
Algorithm: aDyn threshold > 4.0 m/s²
Inputs: Accelerometer
→ 200 ms haptic + cloud event flag
Dwell Detection
Algorithm: Speed < 0.02 m/s timed state
Inputs: Encoder speed
→ Staff alert after 4 s pause
Browsing
Algorithm: Slow + turn rate + dwell combo
Inputs: Encoder + gyro + dwell timer
→ Blue event pill on dashboard
Queue Detection
Algorithm: Creep + low turn + stop-go
Inputs: All sensors fused
→ 300 ms haptic + checkout bay highlight
Step Cadence
Algorithm: Peak detection on |aDyn|
Inputs: Accelerometer
→ Steps per minute in telemetry
Load Proxy
Algorithm: EMA: vibration + jerk + speed
Inputs: Accel + encoder
→ Estimated load level in telemetry

## Slide 6
ACTUATION & RELIABILITY
Actuators & System Health State Machine
ACTUATOR 1
ST7789 TFT Display — 240×240
· Red/white alternating flash at 180 ms intervals
· "ATTENTION — Check trolley — Staff alerted"
· Duration configurable via MQTT: displayFlashMs
· Normal mode: status display (speed, zone, system state)
· Shows live speed (m/s), zone label, and system state
· Remotely disableable via MQTT: { "actuatorEnabled": false }
5-STATE HEALTH MONITOR
System State Machine
NORMAL
All 3 anchors + MQTT connected
DEGRADED
1–2 anchors — reduced positioning accuracy
CLOUD_OFFLINE
MQTT disconnected — edge still operates
NO_ANCHOR
0 anchors — zone classification disabled
IMU_FAIL
IMU init failed — halts with error screen
Auto-recovery: WiFi retry every 10 s · MQTT retry every 1.5 s · DB rollback on write error

## Slide 7
RESOURCE EVALUATION
Power Budget
BATTERY SPEC
1100 mAh Li-Po
Cell voltage
3.7 V
Capacity
1,100 mAh
Energy stored
4.07 Wh
Supply voltage
5 V via boost
Current draw
0.20 A
Active power
1.00 W
Converter eff.
~87%
Usable energy
3.54 Wh
Runtime
~3.5 hours
CURRENT BREAKDOWN
Power Consumers
Wi-Fi radio (always-on)
~150 mA
ST7789 TFT + backlight
~30 mA
ESP32-S3 core
~20 mA
QMI8658 IMU
~1 mA
OPTIMISATION NOTE
· Wi-Fi sleep disabled for MQTT responsiveness
· Enabling DTIM modem sleep → −30–40% power
· Would extend runtime to ~5 hours
· Trade-off: +100 ms reconnect latency
RUNTIME
~3.5 hrs
per charge cycle
4.07 Wh × 0.87 = 3.54 Wh usable
3.54 Wh ÷ 1.0 W = 3.54 hours
Sufficient for a full retail
morning session.
Charge between AM / PM shifts.

## Slide 8
RESOURCE EVALUATION · BANDWIDTH
Proof of Optimised Bandwidth
NAÏVE BASELINE
307.2 Kbps
50 Hz · no rate limiter
OPTIMISED
61.4 Kbps
10 Hz · decoupled upload
REDUCTION
−80%
Less upstream traffic
DATA / SHIFT
94 MB
vs 484 MB naïve (−81%)
Optimisation
What Changed
Impact
Δ
Upload rate decoupling
Sensor 50 Hz stays intact → Upload rate capped at 10 Hz
307 → 61.4 Kbps
−80%
RSSI scan throttling
Every loop tick (infeasible) → Every 15 s (configurable)
20% → 1.3% duty
−93.5%
Speed-gated scanning
Scans during motion → Only when speed < 0.02 m/s
IMU gaps: 10 → 0
−100%
Event-priority upload
Embedded in 100 ms cadence → Immediate at 40 ms gap
Latency: 100→40 ms
−60%
MQTT QoS 1 vs QoS 2
4-packet handshake → 2-packet handshake
200 → 20 ctrl/s
−90%
768 B JSON payload · 28 fields per reading · Future savings: gzip −35% → ~61 MB/shift · CBOR binary −50% → ~47 MB/shift · UDP direct path (port 4210) bypasses MQTT on local LAN

## Slide 9
COMMUNICATIONS & SECURITY
MQTT Stack & Security Architecture
MQTT · PRIMARY CLOUD PATH
Broker
mqtt.yungcz.com : 8883
Protocol
MQTT over TLS 1.3 (RFC 8446)
CA cert
ISRG Root X1 — pinned in firmware
Auth
Username + password
Publish
smarttrolley/trolley_01/telemetry
Subscribe
smarttrolley/trolley_01/config
QoS
1 — at-least-once
Reconnect
Every 1.5 s on disconnect
WHY SECURITY IS NECESSARY
· Config topic is an attack surface — rogue client could disable actuators
· Telemetry contains privacy-sensitive movement & dwell data
· Publicly accessible device on Wi-Fi — TLS prevents sniffing
TLS 1.3 Encryption
IETF RFC 8446 · all MQTT traffic encrypted · 1-RTT handshake
CA Certificate Pinning
ISRG Root X1 hardcoded in firmware — prevents MITM attacks
Broker Authentication
Username + password on every connect · topic-level isolation
Payload Validation
FastAPI + Pydantic validates all inbound config API calls
Error Isolation
Malformed MQTT / UDP payloads caught & discarded gracefully
AWS RDS Security
Database in private subnet (VPC) — not publicly reachable

## Slide 10
DASHBOARD & ANALYTICS
Dashboard Features & Metabase Analytics
Live Monitoring
· Speed · cadence · distance · dwell time
· Zone: A / B / C / BETWEEN / UNKNOWN
· RSSI bars for all 3 anchors
· State badge: NORMAL / DEGRADED / OFFLINE
· Event pills: Pickup · Drop · Browsing · Queue
· WebSocket push — updates in < 250 ms
Store Heatmap & Queue
· Gaussian KDE over 6×6 m SVG floor plan
· Shelf rows + 3 checkout bays mapped
· Switches to Queue Status on queue_detect
· Highlights active checkout bay + dwell time
· Expandable to 500×500 px full modal
· Session density from RSSI trilateration
External Context
· Open-Meteo API — refreshed every 5 min
· Temperature · feels-like · wind · rain
· Sunrise / sunset / daylight hours
· Part-of-day & shopping period labels
· Weekday vs weekend classification
· Weather chip always visible in nav bar
Metabase Analytics
· analytics.cartly.yungcz.com (EC2)
· Connected directly to AWS RDS MySQL
· Telemetry volume over time
· Average speed · zone distribution
· Queue events by hour of day
· Pickup vs drop event counts
Export: GET /api/telemetry/export?format=csv · GET .../export?format=json · All 28 columns · streamed from AWS RDS MySQL

## Slide 11
DESIGN RATIONALE
Evidence-Informed Design Choices
RSSI Trilateration
Log-distance path loss — Rappaport (2002)
RSSI(d) = RSSI(d₀) − 10n·log₁₀(d/d₀) · n = 2.2 (open retail) · d₀ = 1 m @ −56 dBm measured empirically
EMA Filtering
O(1) noise rejection vs SMA
α = 0.1–0.3 tuned empirically · Applied to: speed, vibration RMS, jerk, turn rate, cadence
Gravity Removal
Dynamic accel isolation — Bao & Intille (2004)
aDyn = raw accel − EMA(gravity) · Prevents false pickup/drop triggers on a tilted trolley
MQTT Protocol
ISO/IEC 20922 — purpose-built for constrained IoT
QoS 1 guarantees delivery without QoS 2 double-handshake overhead · Pub/sub = natural access control
TLS 1.3
IETF RFC 8446 · OWASP IoT cert pinning guidance
1-RTT vs TLS 1.2 2-RTT · Critical for 1.5 s MQTT reconnect cycle · ISRG Root X1 pinned in firmware
Empirical Calibration
All thresholds set via repeated physical tests
Pickup 2.5 m/s² · Drop 4.0 m/s² · Queue dwell 3 s · Encoder CPR manually verified · Wheel ⌀ caliper-measured

## Slide 12
CLOUD ARCHITECTURE
AWS Stack — Deployed & Proposed
CURRENTLY LIVE
✓ LIVE
AWS RDS MySQL
eu-west-2 · cartly-database.czoceemm8dli.eu-west-2.rds.amazonaws.com : 3306
✓ LIVE
EC2 Backend API
eu-west-2 · api.cartly.yungcz.com (FastAPI + paho-mqtt + SQLAlchemy)
✓ LIVE
Metabase Analytics
EC2-hosted · analytics.cartly.yungcz.com — connected to RDS MySQL
PROPOSED ADDITIONS
AWS IoT Core
Managed MQTT — scalable, Lambda-integrated
AWS QuickSight
BI dashboards over RDS — no extra ETL
AWS S3
Long-term CSV/parquet archival from RDS
AWS Lambda
Event triggers on queue_detect / pickup
AWS Cognito
Dashboard auth — staff vs manager roles
END-TO-END DATA FLOW
How data moves through the system
ESP32-S3 Sensors
50 Hz IMU · encoder · RSSI
↓
MQTT TLS 1.3
mqtt.yungcz.com:8883 · QoS 1 · 10 Hz
↓
FastAPI Backend
api.cartly.yungcz.com · WebSocket
↓
AWS RDS MySQL
eu-west-2 · 28 cols · timestamped
↓
React Dashboard
Live WebSocket · < 250 ms latency
↓
Metabase Analytics
analytics.cartly.yungcz.com · SQL BI
↓
Open-Meteo API
Weather enrichment · 5 min cache

## Slide 13
ASSESSMENT
Marking Criteria — All Covered
Category
Criterion
Evidence
✅ Specifications
Key user requirements & KPIs
Rappaport·Bao·RFC8446·OWASP refs
✅ Specifications
Deployment challenges considered
Battery life·anchors·MQTT retry·TLS
✅ Specifications
Evidence-informed design choices
Literature + empirical calibration
✅ End-to-End
≥4 sensor types
Accel · Gyro · RSSI · Encoder
✅ End-to-End
≥1 actuator + MKR1010 board
TFT display · 2×MKR1010 + 1×C3 as APs
✅ End-to-End
Data transmitted to cloud
MQTT TLS → mqtt.yungcz.com → RDS
✅ Data
Online database
AWS RDS MySQL eu-west-2
✅ Data
Labelled for analysis
28 named columns + timestamp
✅ Data
Time-series download
/api/telemetry/export?format=csv
✅ UI
Operational dashboard
React · live WS · heatmap · config
✅ UI
Sensors trigger interface actions
Alert pills · state badge · WS push
✅ UI
Remote control of edge system
6 presets + custom → MQTT config
Category
Criterion
Evidence
✅ Edge Control
Dynamically configurable, any location
MQTT config sub · OTA · no reboot
✅ Edge Control
Manual & automatic actuation
Config panel + on-device classifiers
✅ Resources
Estimated power consumption
5V×0.2A=1W · 3.54Wh÷1W=3.5hr
✅ Resources
Proof of optimised bandwidth
307→61 Kbps (−80%) · 5 optimisations
✅ Optimised
Wireless sensor network
2×MKR1010 + 1×C3 + ESP32-S3 star topology
✅ Optimised
Battery powered
1100mAh Li-Po · 3.5hr runtime
✅ Enriched
External data sources
Open-Meteo API · weather · daylight
✅ Enriched
Failsafe mechanisms
5-state machine · reconnect · rollback
✅ Enriched
Analytics platform
Metabase @ analytics.cartly.yungcz.com
✅ Security
Security protocols + why
TLS 1.3 · CA pin · auth · isolation
✅ Security
AWS tools described
RDS live · IoT Core/QS/S3 proposed

## Slide 14
LIVE DEMONSTRATION
Demo Script — Talking Points
01
End-to-End Flow
Move trolley → 50 Hz sensors → 8 classifiers → MQTT TLS 10 Hz → AWS RDS → dashboard WebSocket < 250 ms
02
Edge Intelligence
Trigger pickup — haptic fires immediately with no cloud round-trip. Show on-device actuation is instant.
03
Dynamic Reconfiguration
Config panel: change pickupAccelThreshold → MQTT publish → device applies instantly → repeat pickup gesture.
04
Positioning & Heatmap
Walk zones A→B→C: RSSI + zone badge change. Expand heatmap to show session trail on 6×6 m floor plan.
05
Queue Detection
Enter checkout area → queue_detect fires → dashboard switches to Queue Status view → bay highlighted + dwell.
06
External Context
Show weather panel: Open-Meteo live temperature/rain/cloud + shopping period label in nav bar chips.
07
Power & Battery
1100 mAh @ 3.7V → 1W draw → 3.5 hr runtime at 5V × 0.2A. Sufficient for retail morning shift.
08
Security Demo
MQTT runs over TLS 1.3. ISRG Root X1 CA pinned in firmware. AWS RDS in private VPC subnet.
09
Data Export
Click Download CSV → full time-series streamed from AWS RDS · 28 labelled columns · all readings.
10
Failsafe Demo
Disconnect Wi-Fi → CLOUD_OFFLINE badge. Reconnect → NORMAL within 1.5 s. Edge keeps running throughout.
11
Metabase Analytics
Open analytics.cartly.yungcz.com → show speed trends, zone distribution, queue events by hour from AWS RDS.
12
Anchor Node Role
2× Arduino MKR1010 + 1× ESP32 C3 Super Mini = infrastructure APs. Each broadcasts a fixed SSID. Trolley scans RSSI every 15 s.

## Slide 15
TECHNICAL STACK
Full Technical Stack
Infrastructure
2× MKR1010 + 1× ESP32 C3
Wi-Fi APs · ANCHOR_A/B/C
Edge MCU
ESP32-S3
50 Hz loop · 8 classifiers · C++
IMU
QMI8658 (6-axis, I²C)
Accel + Gyro · GPIO 47/48
Display
ST7789 240×240 TFT (SPI)
Status + alert flash
Firmware
C++ · Arduino · PlatformIO
PubSubClient · Arduino_GFX
Cloud Transport
MQTT over TLS 1.3
PubSubClient · ISRG Root X1 pinned
Local Transport
UDP JSON · port 4210
Opt-in · 20 Hz · bypasses broker
Backend
Python FastAPI + SQLAlchemy
api.cartly.yungcz.com
Database
AWS RDS MySQL (eu-west-2)
cartly-database.czoceemm8dli…
Analytics
Metabase on EC2
analytics.cartly.yungcz.com
External Data
Open-Meteo Forecast API
Weather · free · no API key needed
MQTT Client
paho-mqtt
Backend subscriber · TLS verified
Frontend
React + Recharts + WS
api.cartly.yungcz.com (cloud-hosted)
Build
PlatformIO
ESP32-S3 Arduino target
Cartly · ELEC0033 · UCL Year 3 · Edge Demonstration · All marking criteria ✅